## Verification of correct voxel mapping

We want to verify that we can accurately identify corresponding voxels between the input and output in Novi-sim. The input is one or more STL models that each represent some material in our sample. The output is a reconstructed tomogram containing the “scanned” sample.
Full pipeline is: (Numpy array→STL→Novi-Sim→Reconstruction→Numpy array)
On the surface it may appear trivial that these should have a 1-to-1 mapping, but due to the complex nature of the acquisition setup settings in Novi-Sim’s simulator, this is not obviously the case. This document serves to convince ourselves that we indeed have a correct mapping.

Numpy masks

- Size of both 3d arrays: (500,500,500) pixels
- Outer shell thickness: 5 pixels
- Inner solid cube lengths: (100,100,100) pixels
- Padding between shell and frame: (100,100,100) pixels
- Intermediate frame thickness: 20 pixels
- Intermediate frame lengths: 300 pixels
- Mask is binary, so only 0’s and 1’s

Imported STL to Novi-sim

Acquisition setup
- ROI: 800x800x800 ROI
- Distances: Total 1m, source-sample: 60cm, sample-detector: 40 cm
- Pixel size in scintillator plan: 120 µm (ROI multiplied with this gives projections image size)
- Pixelsize at rotation axis: 72 µm (1 px in tomogram is thus 0.072 mm)
  Sensor
- Pixel pitch (hor,ver): (120,120) µm (this fixes “pixelsize in scintillator plan”, but apparently only horizontal value has effect?)
  PSF (Gaussian)
- FWHM: 1.5 pixels
  Sample
- Scale determines sample size (for example in mm), and this fully reflects the size of the sample in the final reconstructed tomogram slice.
  Reconstruction
- Voxel size (x,y,z): (72,72,72) µm (unless set to manual, it is determined by “pixel size at rotation axis”)
- ROI (x,y,z): (800,800,800) voxels
- Offset (x,y,z): (0,0,0) voxels